Stream Revitalization: Principals and Practices

143SRPP: Winter 2019

Homework Question Set No. 3

Short answers to questions. Suggested length is dependent on question, typically one to two sentences, and for some questions the length may be a paragraph.

Assigned on 11 November 2019  /  Due  on 25 November 2019

- What are the major forces applied to a non-cohesive sediment particle on rest at the bottom of a flowing stream ?

- What is the critical Shields parameter ?

- What is the difference between bedload transport and suspended sediment transport ?

- Bedload sediment discharge equations are similar how ?

- Sediment deposition is based on fall velocity, what are the physical parameters that control fall velocity of a sediment particle ?

- What are the differences between dominant discharge, effective discharge, and bankfull discharge; what are any similarities ?

- What are the three major concepts that initiate and/or maintain pool-riffle sequences ?

- Describe helical flow patterns through a pool-riffle sequence.

- Describe the effect of curvature on hydraulics in a river bend, and how does it influence secondary flow patterns according to Dietrich (1983).

- Describe bed shear stress patterns through a meander and its influence on sediment transport sorting according to Dietrich (1983).

- What is the bar-bend theory ?

- What are the main variables for the hydraulic geometry equations ?

- What is the difference between downstream and at-a-point hydraulic geometry ?

- Describe the six stages delineated in the channel evolution model (CEM) as described by Simon (and Schumm).

- How did Cluer and Thorne (2014) revise the Channel Evolution Model change from that of Simon’s original concept ?